## Slide 1: Biomedical and Electrical Engineering – Robotic Control in Medicine
Launchpad workshop

## Slide 2: Biomedical Robotics
Example applications
  Knee prosthesis implant surgery
  Dental surgery
  Robotic arm prosthesis
  “Neural prosthesis” through brain-computer interface
Core components:
  Microcontrollers
  Sensors - Sense information from the patient’s body or the patient’s environment
  make decisions, e.g.:
    how to move a surgical tool, or
    how to deliver an electrical therapy
    how much medicine to deliver
    how to move a device designed to assist people who cannot move their legs or arms
Image credit: Chris Newmarker, The Robot Report

## Slide 3: Scientific Questions to Answer Today
What are applications of medical robotics?
What are microcontrollers and why are they useful?
What are examples of sensors that could be used in medicine?
How do we make robots and devices carry out desired actions?
  How do we make a pump run without manual human labor?
  How do we move an object (arm) where we want it to go?
  How do we make a robot know when to stop (or start) on its own?

## Slide 4: Today’s Lab Activity
Shampoo Dispensing
  DC Motor to Power Supply
Arm Position
  Stepper Motor
Scrub
  Servo motor
Feedback control with Gripper
  Servo Motor
  FSR

## Slide 5: Shampoo Dispensing
Control flow rate:
  Before connecting anything, turn power supply on. Select Output On and +25 V button. Adjust the knob to 0V. Then turn off power supply.
  Connect DC motor to power supply with power supply off. Red banana cable to the power supply and red alligator clip to white motor lead. Black banana cable to the power supply and black alligator clip to brown motor lead.
  Turn power supply on, follow the same steps and gradually adjust the voltage control knob clockwise. Control decimal to the nearest 10th by using the right arrow. Log results.
  Turn off and attach the pump (plastic housing) and tubing. Dip the inlet tubing into the shampoo and the outlet tubing into the empty graduated cylinder.
  Turn power supply on and increase the voltage until the shampoo starts moving through the tubing.
  Determine flow rate by timing how long it takes to fill graduated cylinder with 10mL of shampoo. Log results

## Slide 6: Shampoo Dispensing
Control timing:
  Empty and wash out graduated cylinder.
  Disconnect the positive power supply lead.
  Add the push button in series.
  Based on flow rate, determine how long to turn pump on in order to get 8mL of shampoo dispensed.
  Set timer for partner to turn the switch off to get 8mL of shampoo dispensed.
  Have your partner turn her back to the graduated cylinder and turn the switch on, time the designated duration, and then switch the pump off when she thinks 8mL has been dispensed. Log results.

## Slide 7: Switch in Series

## Slide 8: Position Arm – Stepper Motor
  Controlling angular position of stepper motor
    Connect the stepper motor to the motor shield according to wiring diagram in Fig. 1
    Connect the Arduino board to the laptop and connect the power supply to the motor shield.
    Launch Arduino.
    Click Tools → Board → Arduino Uno
    Click Tools → Port → COMX (Arduino Uno)
    Save your code
    Click Verify (✓)
    Click Upload (🡆)
WARNING: MOTOR SHIELD and STEPPER MOTOR gets hot! Do not touch the motor or chips!
If you need any assistance with wiring, please let a student facilitator know if you're in need of any help.

## Slide 9: Position Arm – Stepper Motor
  Control angular position
    Click Tools → Serial Monitor
    Type “Start Motor” hit enter
    Type END hit enter stepper motor should start moving
    Type “Stop Motor” hit enter
    Type END hit enter to stop motor
  Change the orientation and speed
    Now, see if you can adjust one number in the code to get the stepper motor to be positioned counterclockwise and speed
    Log results

## Slide 10
Position Arm – Stepper Motor​
  Control linear position
  Now, see if you can adjust one number in the code to get the arm jig to be positioned at certain points along the rail:
    approximately halfway across and
    ~¼ of the way across.​
  Log results.​

## Slide 11: Scrub – servo motor
View and predict PWM output
Wire servomotor to Pynq board as shown in Fig. 2.
Connect the PWM output to the oscilloscope. In your workbook, sketch the output you predict to see.
Now run servoGo.ipynb and log results.
Adjust the code to make it scrub for 5s.
Adjust the code to make the arm scrub more of the back (i.e., control the length along back that it scrubs)
Adjust the code to make arm scrub faster.
Log results.
Log results.
Figure 1

## Slide 12: Feedback control with gripper
Open and close gripper
  On your Yoga tablet, open the Arduino app
  In C:\LaunchPadBW\ => find and open gripper.ino.
  Run through the code and observe the actions of the gripper. The gripper should open and close.
  Find the place in the code where the gripper position (or how wide the gripper is open or closed) is controlled.
  In your worksheet, plan how you will adjust the code to try to get the gripper to close on the sponge and be able to hold the sponge without squishing the sponge. Then implement the code changes. In order to test out how well you managed to get your controller to hold onto something without squashing it, you will actually use your finger in place of the sponge. When the gripper is wide open, insert your index finger.
  Log results.

## Slide 13: Feedback control with gripper
  Adding the FSR: voltage divider output
    Wire the voltage divider circuit with the FSR as shown in Fig. 3
    Plug in the Arduino board so that now the 5V supply to your circuit board is on.
    Gradually push harder and softer on the FSR. Log results. What do you see on the oscilloscope as you push harder on the FSR? As you release the FSR?
Figure 3

## Slide 15: Feedback control with Gripper
Get gripper to hold sponge with right amount of pressure
  Open pressureSensing.ino
  Adjust the code so that the gripper will stop closing when the FSR senses pressure against the sponge.
  Holding the terminal end (not the sensor end), hold the FSR sensor portion against the sponge. Run the code and test whether the gripper is able to automatically stop closing when it reaches the desired pressure. Log results.